SM
Instruction Cache
Warp Scheduler
Warp Scheduler
Dispatch Unit
Dispatch Unit
Register File (32,768 x 32-bit)
CUDA Core
LD/ST
Core
Core
Core
Core
Dispatch Port
LD/ST
SFU
Operand Collector
LD/ST
Core
Core
Core
Core
LD/ST
FP Unit
INT Unit
LD/ST
Core
Core
Core
Core
LD/ST
Result Queue
SFU
LD/ST
Core
Core
Core
Core
LD/ST
LD/ST
Core
Core
Core
Core
LD/ST
SFU
LD/ST
Core
Core
Core
Core
LD/ST
LD/ST
Core
Core
Core
Core
LD/ST
SFU
LD/ST
Core
Core
Core
Core
LD/ST
Interconnect Network
64 KB Shared Memory / L1 Cache
Uniform Cache
Tex
Tex
Tex
Tex
Texture Cache
PolyMorph Engine
Viewport
Vertex Fetch
Tessellator
Transform
Attribute Setup
Stream Output

---
GPC
Raster Engine
SM
SM
SM
SM
Polymorph Engine
Polymorph Engine
Polymorph Engine
Polymorph Engine
Graphics Processing Cluster (GPC)

---
Host Interface
GigaThread Engine
GPC
GPC
Raster Engine
Raster Engine
SM
SM
SM
SM
SM
SM
SM
SM
Polymorph Engine
Polymorph Engine
Polymorph Engine
Polymorph Engine
Polymorph Engine
Polymorph Engine
Polymorph Engine
Polymorph Engine
L2 Cache
Polymorph Engine
Polymorph Engine
Polymorph Engine
Polymorph Engine
Polymorph Engine
Polymorph Engine
Polymorph Engine
Polymorph Engine
SM
SM
SM
SM
SM
SM
SM
SM
Raster Engine
Raster Engine
GPC
GPC
GF100 block diagram showing the Host Interface, the GigaThread Engine, four GPCs, six Memory Controllers, six ROP partitions,
and a 768 KB L2 cache. Each GPC contains four PolyMorph engines. The ROP partitions are immediately adjacent to the L2 cache.
Memory Controller
Memory Controller
Memory Controller
Memory Controller
Memory Controller
Memory Controller

---
JETSON SUCCESS STORIES
Healthcare
Construction
Agriculture
Smart City
Industrial
Aerospace/Defense
Inventory Mgmt
Delivery
Inspection
Service
Retail
Logistics

---
ANNOUNCING:
JETSON NANO
Small, low-power AI Computer
128 CUDA Cores | 4 Core CPU
4 GB Memory
472 GFLOPs
70x45mm
5W | 10W
$129
6

---
JETSON NANO SPECIFICATIONS
128 Core Maxwell
GPU
472 GFLOPs (FP16)
CPU
4 core ARM A57 @ 1.43 GHz
Memory
4 GB 64 bit LPDDR4 25.6 GB/s
Storage
16 GB eMMC
4K @ 30 | 4x 1080p @ 30 | 8x 720p @ 30
Video Encode
(H.264/H.265)
4K @ 60 | 2x 4K @ 30 | 8x 1080p @ 30 | 16x 720p @
Video Decode
30 | (H.264/H.265)
12 (3x4 or 4x2) MIPI CSI-2 DPHY 1.1 lanes
Camera
(1.5 Gbps)
HDMI 2.0 or DP1.2 | eDP 1.4 | DSI (1 x2)
Display
2 simultaneous
1 x1/2/4 PCIE
UPHY
1 USB 3.0
Other I/Os
1xSDIO / 2xSPI / 3xI2C / UART / I2S / GPIOs
7

---
JETSON NANO RUNS MODERN AI
Inference
50
40
30
20
10
0
Resnet50
Inception v4
VGG-19
SSD
SSD
SSD
Tiny Yolo
Unet
Super
OpenPose
Mobilenet-v2
Mobilenet-v2
Mobilenet-v2
resolution
(300x300)
(960x544)
(1920x1080)
Coral dev board (Edge TPU)
Raspberry Pi 3 + Intel Neural Compute Stick 2
Jetson Nano
Not supported/DNR
9
Img/sec

---
THE JETSON FAMILY
From AI at the Edge to Autonomous Machines
JETSON TX1
JETSON TX2 4 GB
JETSON TX2 8GB | Industrial
JETSON AGX XAVIER
JETSON NANO
→
7 - 15W
7 – 15W
10 – 30W
5 - 10W
1 – 1.3 TFLOPS (FP16)
1.3 TFLOPS (FP16)
10 TFLOPS (FP16) | 32 TOPS (INT8)
0.5 TFLOPS (FP16)
50mm x 87mm
50mm x 87mm
100mm x 87mm
45mm x 70mm
$299
$399 - $749
$1099
$129
AI at the edge
Fully autonomous machines
Multiple devices - Same software
11
Listed prices are for 1000u+ | Full specs at developer.nvidia.com/jetson

---
JETSON NANO
JETSON TX1
JETSON TX2
JETSON AGX XAVIER
512 Core Volta + NVDLA
128 Core Maxwell
256 Core Maxwell
256 Core Pascal
GPU
10 TFLOPS (FP16)
0.5 TFLOPs (FP16)
1 TFLOPS (FP16)
1.3 TFLOPS (FP16)
32 TFLOPS (INT8)
8 core Carmel ARM CPU @
4 core ARM A57
4 core ARM A57
6 core Denver and A57 @
CPU
2.26GHz
(1.5 GHz)
(1.5 / 1.7 GHz)
2GHz (2x) 2MB L2
(4x) 2MB L2 + 4MB L3
4 GB 128
8 GB 128
16GB 256-bit LPDDR4x @
4 GB 64 bit LPDDR4
4 GB 64 bit LPDDR4
Memory
bit LPDDR4
bit LPDDR4
2133MHz
25.6 GB/s
25.6 GB/s
51 GB/s
58 GB/s
137 GB/s
16 GB
32 GB
Storage
16 GB eMMC
16 GB eMMC
32 GB eMMC
eMMC
eMMC
Video Encode
4K @ 30 (H.264/H.265)
4K @ 30 (H.264/H.265)
2x 4K @ 30 (HEVC)
8x 4K @ 60 (HEVC)
Video Decode
4K @ 60 (H.264/H.265)
4K @ 60 (H.264/H.265)
2x 4K @ 30 12 bit support
12x 4K @ 30 12-bit support
16 lanes MIPI CSI-2 | 8
12 (3x4 or 4x2) MIPI CSI-2
12 (3x4 or 6x2) MIPI CSI-2
12 lanes MIPI CSI-2
lanes SLVS-EC
Camera
DPHY 1.1 lanes (1.5 Gbps)
DPHY 1.1 lanes (1.5 Gbps)
D-PHY 1.2 (30 Gbps)
D-PHY (40 Gbps)
C-PHY (109 Gbps)
69.6mm x 45mm
87mm x 50mm
87mm x 50mm
100mm x 87mm
Mechanical
260 pin edge connector
400 pin connector
400 pin connector
699 pin connector
Software
Jetpack SDK – Unified software release across all Jetson products
15
Softwa
re

---
JETSON NANO DEVELOPER KIT
$99 AI Computer
128 CUDA Cores | 4 Core CPU
472 GFLOPs
5W | 10W
Available from nvidia.com and
distributors worldwide
17

---
Figure 2.1: Graphics pipeline after shaders inclusion.

---
SM
Host Interface
Instruction Cache
GigaThread Engine
Warp Scheduler
Warp Scheduler
GPC
GPC
Dispatch Unit
Dispatch Unit
Raster Engine
Raster Engine
Register File (32,768 x 32-bit)
SM
SM
SM
SM
SM
SM
SM
SM
CUDA Core
LD/ST
Core
Core
Core
Core
Dispatch Port
LD/ST
SFU
Operand Collector
LD/ST
Core
Core
Core
Core
LD/ST
FP Unit
INT Unit
LD/ST
Core
Core
Core
Core
LD/ST
Result Queue
SFU
LD/ST
Core
Core
Core
Core
LD/ST
PolyMorph Engine
PolyMorph Engine
PolyMorph Engine
PolyMorph Engine
PolyMorph Engine
PolyMorph Engine
PolyMorph Engine
PolyMorph Engine
LD/ST
Core
Core
Core
Core
LD/ST
SFU
L2 Cache
LD/ST
Core
Core
Core
Core
LD/ST
LD/ST
Core
Core
Core
Core
LD/ST
PolyMorph Engine
PolyMorph Engine
PolyMorph Engine
PolyMorph Engine
PolyMorph Engine
PolyMorph Engine
PolyMorph Engine
PolyMorph Engine
SFU
LD/ST
Core
Core
Core
Core
LD/ST
Interconect Network
64 KB Shared Memory / L1 Cache
Uniform Cache
Tex
Tex
Tex
Tex
Texture Cache
PolyMorph Engine
SM
SM
SM
SM
SM
SM
SM
SM
Viewport
Vertex Fetch
Tessellator
Transform
Raster Engine
Raster Engine
Attribute Setup
Stream Output
GPC
GPC
Figure 3.6: GF100 block diagram and Stream Multiprocessor detail. [31, pg. 11 and 16]
Memory Controller
Memory Controller
Memory Controller
Memory Controller
Memory Controller
Memory Controller

---
SMM
PolyMorph Engine 3.0
Vertex Fetch
Tessellator
Viewport Transform
Attribute Setup
Stream Output
Instruction Buffer
Instruction Buffer
Instruction Buffer
Warp Scheduler
Warp Scheduler
Dispatch Unit
Dispatch Unit
Dispatch Unit
Dispatch Unit
Register File (16,384 x 32-bit)
Register File (16,384 x 32-bit)
Core
Core
Core
Core
LD/ST
SFU
Core
Core
Core
Core
LD/ST
SFU
Core
Core
Core
Core
LD/ST
SFU
Core
Core
Core
Core
LD/ST
SFU
Core
Core
Core
Core
LD/ST
SFU
Core
Core
Core
Core
LD/ST
SFU
Core
Core
Core
Core
LD/ST
SFU
Core
Core
Core
Core
LD/ST
SFU
Core
Core
Core
Core
LD/ST
SFU
Core
Core
Core
Core
LD/ST
SFU
Core
Core
Core
Core
LD/ST
SFU
Core
Core
Core
Core
LD/ST
SFU
Core
Core
Core
Core
LD/ST
SFU
Core
Core
Core
Core
LD/ST
SFU
Core
Core
Core
Core
LD/ST
SFU
Core
Core
Core
Core
LD/ST
SFU
Texture/L1 Cache
Tex
Tex
Tex
Tex
Instruction Buffer
Instruction Buffer
Warp Scheduler
Warp Scheduler
Dispatch Unit
Dispatch Unit
Dispatch Unit
Dispatch Unit
Register File (16,384 x 32-bit)
Register File (16,384 x 32-bit)
Core
Core
Core
Core
LD/ST
SFU
Core
Core
Core
Core
LD/ST
SFU
Core
Core
Core
Core
LD/ST
SFU
Core
Core
Core
Core
LD/ST
SFU
Core
Core
Core
Core
LD/ST
SFU
Core
Core
Core
Core
LD/ST
SFU
Core
Core
Core
Core
LD/ST
SFU
Core
Core
Core
Core
LD/ST
SFU
Core
Core
Core
Core
LD/ST
SFU
Core
Core
Core
Core
LD/ST
SFU
Core
Core
Core
Core
LD/ST
SFU
Core
Core
Core
Core
LD/ST
SFU
Core
Core
Core
Core
LD/ST
SFU
Core
Core
Core
Core
LD/ST
SFU
Core
Core
Core
Core
LD/ST
SFU
Core
Core
Core
Core
LD/ST
SFU
Texture/L1 Cache
Tex
Tex
Tex
Tex
96KB Shared Memory
Figure 3.12: GM204 SMM Diagram (GM204 also features 4 DP units per SMM, which are
not depicted on this diagram). NVIDIA Corporation [41, pg. 08]

---
PCI Express 3.0 Host Interface
GigaThread Engine
SMM
SMM
SMM
SMM
SMM
SMM
SMM
SMM
Raster Engine
Raster Engine
GPC
GPC
L2 Cache
SMM
SMM
SMM
SMM
SMM
SMM
SMM
SMM
Raster Engine
Raster Engine
GPC
GPC
Figure 3.13: Maxwell GK204 full chip block diagram.NVIDIA Corporation [41, pg. 06]
Memory Controller
Memory Controller
Memory Controller
Memory Controller