## Slide 3
 | Myriad 2 | Myriad X
Compute Capacity | >1 TOPS | >4 TOPS
Vector Processors | 12x SHAVE Processors | 16x SHAVE Processors
CPUs | 2x LEON4 cores (RISC; SPARC V8) | 2x LEON4 cores (RISC; SPARC V8)
On-chip Accelerators | ~20 image/vision processing accelerators | 20+ image/vision processing accelerators, Neural Compute Engine (DNN accelerator)
Neural Network Capability | 1st Gen DNN Support (Up to 100 GFLOPS) | Neural Compute Engine (Up to 1 TOPS)
On-chip Memory and Bandwidth | 2 MB (400 GB/sec) | 2.5 MB (450 GB/sec)
Video | VGA, 720p, 1080p, H.264 (software encoder) | M/JPEG 4K at 60 Hz encoder, H.264/H.265 4K at 30 Hz encoder
Process | 28 nm HPC+/HPC/HPM (TSMC) | 16 nm FFC (TSMC)
Myriad X vs Myriad 2
The Myriad X chip used on the AI CORE X is the successor to the Myriad 2 chip

## Slide 16
搶下新加坡智慧路燈標案，凌華成台灣唯一Google AI晶片Edge TPU合作廠

## Slide 27
Nvidia
Tesla
Fermi
Kepler
Maxwell
Pascal
Volta
Turing

## Slide 30
Figure 1 Jetson Nano Block Diagram
Jetson
3.3V Reg
Nano
Power
Subsystem
PMIC MAX77620
DC Jack
USB
RJ45 w/Magnetics
PCIe x4
LPDDR4
4GB
CPU Reg uP1666
GPU Reg uP1666
eMMC
16GB
Power Monitor
Connectivity
Displays
Gigabit
Ethernet
Cameras
Tegra X1
Misc Expansion
Debug Serial
Port
NOTE:
Not all interfaces shown are available at same time; several interfaces are shown in multiple locations to illustrate different options. See the NVIDIA Jetson Nano OEM Product Design Guide and Pinmux Configuration Spreadsheet for supported options.
JTAG Test Points
* UART
CSI, 3 x4 lane
* CAM I2C–3.3V
CAM MCLK x2
GPIOs/Control
AUDIO MCLK
I2S x2 *
I2C x2–1.8V *
I2C x2–3.3V *
SPI1 x2
*
UART x3
GPIOs/Control
DSI, 2-lane
eDP/DP
DP/HDMI
DP_AUX/DDC
CEC, HPD x2
GPIOs/Control
PCIe *
USB 2.0 *
I2S *
SDIO
UART *
GPIOs/Control
* PCIe x4
GBE_MDI
* USB 2.0 x3
USB 3.0 x1
VDD_IN