## Slide 1
Jetson Nano System-on-Module
Maxwell GPU + ARM Cortex-A57 + 4GB LPDDR4 + 16GB eMMC
1.0 Functional Overview
Designed for use in power-limited environments, the Jetson Nano squeezes industry-leading compute capabilities, 32-bit and
64-bit operating capability, and integrated advanced multi-function audio, video and image processing pipelines into a 260-pin SO-DIMM. The Maxwell GPU architecture implemented several architectural enhancements designed to extract maximum performance per watt consumed. Core components of the Jetson Nano series module include:
NVIDIA® Tegra® X1 series SoC

-
-
NVIDIA Maxwell GPU
ARM® quad-core Cortex®-A57 CPU Complex







4GB LPDDR4 memory
16GB eMMC 5.1 storage
Gigabit Ethernet (10/100/1000 Mbps)
PMIC, regulators, power and voltage monitors
260-pin keyed connector (exposes both high-speed and low-speed industry standard I/O)
On-chip temperature sensors
Board ID EEPROM
Figure 1 Jetson Nano Block Diagram
Jetson
3.3V Reg
Nano
Power
Subsystem
PMIC MAX77620
DC Jack
USB
RJ45 w/Magnetics
PCIe x4
LPDDR4
4GB
CPU Reg uP1666
GPU Reg uP1666
eMMC
16GB
Power Monitor
Connectivity
Displays
Gigabit
Ethernet
Cameras
Tegra X1
Misc Expansion
Debug Serial
Port
JETSON | NANO | DATASHEET | DS-09366-001_v0.1 | SUBJECT TO CHANGE | COPYRIGHT © 2014 – 2019 NVIDIA CORPORATION. ALL RIGHTS RESERVED.
5
NOTE:
Not all interfaces shown are available at same time; several interfaces are shown in multiple locations to illustrate different options. See the NVIDIA Jetson Nano OEM Product Design Guide and Pinmux Configuration Spreadsheet for supported options.
JTAG Test Points
* UART
CSI, 3 x4 lane
* CAM I2C–3.3V
CAM MCLK x2
GPIOs/Control
AUDIO MCLK
I2S x2 *
I2C x2–1.8V *
I2C x2–3.3V *
SPI1 x2
*
UART x3
GPIOs/Control
DSI, 2-lane
eDP/DP
DP/HDMI
DP_AUX/DDC
CEC, HPD x2
GPIOs/Control
PCIe *
USB 2.0 *
I2S *
SDIO
UART *
GPIOs/Control
* PCIe x4
GBE_MDI
* USB 2.0 x3
USB 3.0 x1
VDD_IN